## Slide 1
ARM Cortex-M7 / STM32H7 Series
HSE
4–48 MHz
HSI
64 MHz
LSE
32.768 kHz
LSI
32 kHz
CSI
4 MHz
PLL1 / PLL2 / PLL3
(×N ÷M ÷P/Q/R)
SYSCLK Mux ➜ SYSCLK (up to 480 MHz)
AHB (÷1–512) → APB1 (÷1–16) → APB2 (÷1–16) → APB3/4
STM32H7 Clock Tree
User-Level Understanding: HSE · HSI · PLL · SYSCLK · Peripheral Prescalers
Notes: Title slide. The mini diagram at the top previews the full clock tree. Proceed to walk through each stage.

## Slide 2
STM32H7 Clock Tree — Overview
What Is a Clock Tree?
Every digital circuit needs a clock — a periodic signal that synchronizes all operations.
The STM32H7 does not run all circuits at the same frequency. Instead it uses a tree of dividers and multiplexers to derive many different clocks from one or more sources.
The user configures this tree in firmware (via RCC registers or CubeMX) to balance performance, power consumption, and peripheral compatibility.
Mis-configuring the clock tree is one of the most common sources of bugs in embedded systems — peripherals behave unexpectedly or the MCU hangs at startup.
Clock Sources HSE, HSI, CSI, LSE, LSI
PLL Multipliers PLL1, PLL2, PLL3 — boost frequency
System Clock (SYSCLK) Selected by SW bits in RCC_CFGR
Bus Prescalers AHB, APB1, APB2, APB3, APB4
Peripheral Clocks Timers, SPI, UART, ADC, USB…
💡 Key Principle: The STM32H7 can run its CPU (Cortex-M7) at up to 480 MHz while simultaneously running USB at 48 MHz and low-speed peripherals at much lower speeds — all from the same crystal.
Notes: Explain that the clock tree is configured in the Reset and Clock Control (RCC) peripheral. All register access is in the RCC block.

## Slide 3
HSE — High Speed External Clock
What Is HSE?
HSE stands for High Speed External. It uses an external crystal, ceramic resonator, or oscillator connected to the OSC_IN / OSC_OUT pins of the MCU.
Frequency range: 4 MHz to 48 MHz (crystal or resonator). Can also accept an external square-wave clock directly on OSC_IN.
HSE is the preferred clock source for high-accuracy applications because a good crystal provides ±10–30 ppm stability — far better than the internal RC oscillator.
HSE is almost always used as the PLL input in systems that need USB, Ethernet, or precise baud rates (UART, SPI).
Key RCC Registers
RCC_CR
HSEON bit (16)
Enable HSE oscillator
RCC_CR
HSERDY bit (17)
1 = HSE clock is stable & ready
RCC_CFGR
SW[1:0]
Select HSE as SYSCLK source (SW=10)
XTAL
CL1
CL2
STM32H7
MCU
OSC_IN
OSC_OUT
f HSE
→ PLL / SYSCLK
Typical HSE: 8 MHz or 25 MHz crystal
⚡ Startup Tip: Always poll HSERDY before selecting HSE as the clock source. HSE takes 1–10 ms to stabilize depending on crystal quality. If you switch to HSE before it is ready, the MCU will run from an unstable clock and may crash or enter a HardFault.

## Slide 4
HSI — High Speed Internal Clock
What Is HSI?
HSI is a built-in RC (resistor-capacitor) oscillator running at a fixed 64 MHz on the STM32H7. No external components are required.
It is the default clock source after reset — the MCU always starts on HSI, even before any firmware code runs.
Accuracy: ±1% at room temperature after factory calibration. Trimming is available through the HSITRIM field in RCC_ICSCR1 for improved accuracy.
Drawback: RC oscillators drift with temperature and supply voltage. HSI is not suitable for USB or Ethernet without an external reference.
Use case: Bootloaders, early initialization, low-cost designs without a crystal, or as a fallback if HSE fails.
HSE vs HSI at a Glance
Property | HSE | HSI
Frequency | 4–48 MHz | 64 MHz
Accuracy | ±10–30 ppm | ±1% (±10,000 ppm)
Components | Crystal+caps | None
USB capable | ✓ (via PLL) | ✗ (drift too high)
STM32H7 MCU (Internal View)
HSI
64 MHz RC
CSI
4 MHz RC
SYSCLK Mux (SW bits)
SYSCLK → CPU Core
Reset default path
⚠ Calibration Note: The HSI factory-calibrated value is stored in the HSICAL field. Adjust HSITRIM (5-bit field) to shift the frequency ±64 steps of ~40 kHz each, giving fine-tuning capability of about ±2.56 MHz around 64 MHz.

## Slide 5
PLL — Phase Locked Loop (Frequency Multiplier)
How the PLL Works
A PLL takes a reference clock (HSE or HSI) and multiplies it to a much higher frequency. The STM32H7 has three independent PLLs: PLL1, PLL2, PLL3.
Each PLL has three stages:
  ① Pre-divider M: divides the input to the PLL VCO input frequency (1–63 MHz range).
  ② Multiplier N: multiplies the VCO input up to 750–1500 MHz (the VCO frequency).
  ③ Post-dividers P, Q, R: each divides the VCO output independently to create up to 3 output clocks per PLL.
Formula: f_out = f_in / M × N / P (or Q, R)
Example (PLL1 for 480 MHz SYSCLK with 25 MHz HSE):
f_in=25 MHz, M=5 → VCO_in=5 MHz, N=192 → VCO=960 MHz, P=2 → f_out=480 MHz
HSE/HSI
f_in
÷M
(1-63)
VCO
×N
(4-512)
750–1500 MHz
÷P
SYSCLK
(PLL1P)
÷Q
USB, SDMMC
(PLL1Q=48MHz)
÷R
Peripheral Clk
(PLL1R)
STM32H7 has 3 identical PLLs: PLL1 (for CPU), PLL2 (for ADC, DFSDM, SPI), PLL3 (for USB, SAI, USART)
📐 PLL Formula
f_VCO = (f_ref / M) × N f_PLLx_P = f_VCO / P (SYSCLK source) f_PLLx_Q = f_VCO / Q (48 MHz for USB) f_PLLx_R = f_VCO / R (peripheral clock)
⚠ VCO Range Constraint: The PLL VCO must be in 192–836 MHz (wide range) or 150–420 MHz (medium). Always verify f_VCO = f_ref/M × N is within this range before enabling the PLL.

## Slide 6
System Clock — SYSCLK (up to 480 MHz)
SYSCLK Selection
SYSCLK is the master clock of the Cortex-M7 CPU core and the highest-level bus in the clock hierarchy.
It is selected by writing to the SW[1:0] bits in the RCC_CFGR register. The actual switch only happens when the hardware confirms stability (SWS bits reflect the new source).
Sources (SW bits):
00 → HSI (64 MHz, default at reset)
01 → CSI (4 MHz, low-power applications)
10 → HSE (4–48 MHz external crystal)
11 → PLL1_P output (up to 480 MHz)
Maximum SYSCLK for the Cortex-M7 core is 480 MHz (for Run* / OverDrive mode) or 400 MHz in the normal run domain.
HCLK (AHB clock) = SYSCLK / AHB prescaler. CPU actually clocks off HCLK, so SYSCLK and HCLK are often the same when AHB prescaler = 1.
HSI
64 MHz
SW=00
CSI
4 MHz
SW=01
HSE
4–48MHz
SW=10
PLL1_P
≤480 MHz
SW=11
M
U
X
SYSCLK
SW bits select input
💡 Always verify SWS == SW after switching clocks. The hardware only commits when the new source is stable. Reading SWS before it matches SW means the switch is not complete.

## Slide 7
Peripheral Prescalers — AHB, APB1, APB2, APB3, APB4
Why Prescalers?
Not every peripheral can run at 480 MHz. Older or low-speed peripherals have maximum clock limits. Prescalers divide SYSCLK/AHB down to a safe frequency.
Bus Hierarchy (SYSCLK → peripherals):
SYSCLK → AHB (÷1–512) → HCLK (CPU, DMA, Flash, FMC)
HCLK → APB1 (÷1–16) → PCLK1 (TIM2–7, TIM12–14, USART2–5, SPI2–3, I2C1–3, CAN)
HCLK → APB2 (÷1–16) → PCLK2 (TIM1/8, USART1/6, SPI1/4/5, ADC, SDMMC)
HCLK → APB3 (÷1–16) → PCLK3 (LTDC, WWDG1)
HCLK → APB4 (÷1–16) → PCLK4 (SPI6, I2C4, LPUART1, LPTIM2–5, COMP, VREF, SAI4)
Timer clock multiplier: When APBx prescaler > 1, timer clocks are automatically doubled (×2) by hardware — important when calculating timer frequencies!
SYSCLK
480 MHz
AHB ÷1–512
(HCLK ≤240MHz)
APB1
÷1–16
PCLK1 ≤120MHz
TIM2-7, UART2-5
I2C, CAN
APB2
÷1–16
PCLK2 ≤120MHz
TIM1/8, ADC
SPI1, UART1
APB3
÷1–16
PCLK3 ≤120MHz
LTDC, WWDG1
APB4
÷1–16
PCLK4 ≤120MHz
LPUART, I2C4
LPTIM, SAI4
📌 Example: SYSCLK=480MHz, AHB÷2=240MHz, APB1÷2=120MHz. Timer TIM2 kernel clock = 120MHz×2 = 240MHz (APB prescaler>1, so hardware ×2 applies).

## Slide 8
STM32H7 Clock Tree — Full Flow Diagram
HSE
4–48 MHz
(Crystal)
HSI
64 MHz
(Internal RC)
CSI
4 MHz
(Low Power)
LSE
32.768 kHz
(RTC Crystal)
LSI
32 kHz
(Internal RC)
HSI48
48 MHz
(USB ref)
PLL1
CPU / SYSCLK
PLL2
ADC, SPI, DFSDM
PLL3
USB, SAI, USART
SYSCLK Mux (SW bits) → SYSCLK (max 480 MHz)
AHB Prescaler (÷1–512) → HCLK (max 240 MHz) — CPU, DMA, Flash, FMC
APB1
÷1-16
PCLK1
≤120MHz
APB2
÷1-16
PCLK2
≤120MHz
APB3
÷1-16
PCLK3
≤120MHz
APB4
÷1-16
PCLK4
≤120MHz
Independent Clock Domains
LSE / LSI
RTC, IWDG, BKPSRAM
HSI48 / PLL_Q
USB OTG (must be 48 MHz)
PLL2_P / PLL3_P
SAI1/2/3 (Audio)
PLL3_Q / HSI48
FDCAN
PLL3_R / PLL2_R
DFSDM, SPI1–6

## Slide 9
Practical Configuration — 480 MHz from 25 MHz HSE
Configuration Steps
1
Enable HSE:
Set RCC_CR.HSEON=1, poll HSERDY until 1.
2
Configure PLL1:
Set M=5, N=192, P=2. PLL1 source = HSE. VCO = 25/5×192 = 960 MHz. Output = 960/2 = 480 MHz.
3
Enable PLL1:
Set RCC_CR.PLL1ON=1, poll PLL1RDY until 1.
4
Set flash latency:
Set FLASH_ACR.LATENCY to 4 wait states (required at ≥185 MHz with VOS0).
5
Set prescalers:
AHB÷2→240 MHz, APB1÷2, APB2÷2, APB3÷2, APB4÷2 → 120 MHz each.
6
Switch SYSCLK:
Set RCC_CFGR.SW=11 (PLL1_P), poll SWS until =11.
7
Verify:
Read SystemCoreClock or check with HAL_RCC_GetSysClockFreq() == 480000000UL.
// STM32H7 — 480 MHz from 25 MHz HSE (HAL)
RCC_OscInitTypeDef osc = {0};
osc.OscillatorType = RCC_OSCILLATORTYPE_HSE;
osc.HSEState = RCC_HSE_ON;
osc.PLL.PLLState = RCC_PLL_ON;
osc.PLL.PLLSource = RCC_PLLSOURCE_HSE;
osc.PLL.PLLM = 5; // 25 / 5 = 5 MHz
osc.PLL.PLLN = 192; // 5 × 192 = 960 MHz
osc.PLL.PLLP = 2; // 960 / 2 = 480 MHz
osc.PLL.PLLQ = 10; // 960 / 10 = 96 MHz (USB)
osc.PLL.PLLR = 2; // 960 / 2 = 480 MHz
HAL_RCC_OscConfig(&osc);
RCC_ClkInitTypeDef clk = {0};
clk.ClockType = RCC_CLOCKTYPE_SYSCLK
| RCC_CLOCKTYPE_HCLK
| RCC_CLOCKTYPE_PCLK1
| RCC_CLOCKTYPE_PCLK2;
clk.SYSCLKSource = RCC_SYSCLKSOURCE_PLLCLK;
clk.AHBCLKDivider = RCC_HCLK_DIV2; // 240MHz
clk.APB1CLKDivider = RCC_APB1_DIV2; // 120MHz
clk.APB2CLKDivider = RCC_APB2_DIV2; // 120MHz
HAL_RCC_ClockConfig(&clk, FLASH_LATENCY_4);
⚡ Power domain: 480 MHz requires VOS0 (Voltage Scale 0) via PWR_D3CR. Enable it BEFORE configuring PLL to 480 MHz or the MCU will hard-fault.

## Slide 10
Summary — STM32H7 Clock Tree Key Takeaways
🔷 HSE — External Crystal
Use HSE (4–48 MHz crystal) for precision — USB, Ethernet, UART baud accuracy. Always wait for HSERDY before switching.
🔵 HSI — Internal RC 64 MHz
Default clock at reset. No external parts but ±1% accuracy. Good for bootloaders and non-USB applications.
🔶 PLL — Frequency Multiplier
3 PLLs available. Formula: f_out = (f_in/M)×N/P. VCO must stay 192–960 MHz. Critical for reaching 480 MHz.
⚙️ SYSCLK — Master System Clock
Select source via RCC_CFGR.SW. Max 480 MHz (VOS0). Always poll SWS to confirm the switch completed.
📐 AHB — Bus Clock ÷1–512
HCLK feeds CPU, DMA, Flash. Max 240 MHz. All APB clocks derive from HCLK, so prescale carefully.
🔌 APBx — Peripheral Clocks ÷1–16
APB1–4 each ≤120 MHz. Timer clocks are ×2 when prescaler >1. Configure before enabling peripherals.
🏆 Golden Rule: Source → PLL (multiply) → SYSCLK (select) → AHB (divide) → APBx (divide) → Peripheral. Each stage must be stable before the next is enabled.